## Slide 1: Notes on: Mixed dimensional isogeometric FE-BE coupling analysis for solid–shell structures
Two different ways of mapping of DOFs of solid and shell
Condition of interface equilibrium for constructing ‘monolithic’ stiffness matrix

## Slide 2: Direct kinematic coupling
Translation and rotation fields for shell (in global coordinates system)
Displacement field for Solids (translation only)
(in global coordinates system)
Geometry description for R-M shell

## Slide 3: Weak coupling formulation based on work equality
Force equilibrium condition on the coupling interface

## Slide 4: Weak coupling formulation based on work equality
Discretizing stress resultants
Transform for local coos to global coos

## Slide 5: Governing equations of the coupled system Part 1: Shell - FEM
Rearrange Ku = f. So that are dofs associated with the interface
Integral of body forces and tractions on all surfaces except interface surface
Only traction in the interface

## Slide 6: Governing equations of the coupled system Part 2: Solid - BEM
For BEM, there are no body forces. In paragraph 3.2, it is explained how to rearrange the displacements of BEM. Finally

## Slide 7: Governing equations of the coupled system Final coupling
Direct kinematic coupling
Weak coupling formulation
Finally:

## Slide 8: Notes on: Numerical procedure to couple shell to solid elements by using Nitsche’s method
Notes regards only Shell element MITC4 (method for MITC4ts is the same)
Continuity condition is reached using penalty method
Nitsche method is used to impose the constraint condition

## Slide 9: Continuity condition on connecting surface
Penalty factor

## Slide 10: Traction work on interface is zero
α Nitche parameter

## Slide 11: Variation of potential energy for δυc, δυs

## Slide 12: Incremental form of variational equations

## Slide 14: Goals
Do we want to couple thick or thin elements?
Isogeometric Analysis and Shape Optimal Design of Shell Structures Josef M. Kiendl

## Slide 15: Goals
Do we want monolithic or partitioned coupling?
For monolithic we can implement the same as 1st paper
For partition we can use Mortat based mapping for 1. displacements and 2. force equilibrium (integrals of tractions of solid and shell)
The difference is that solid will use B-spline basis functions (QuEso) and shell NURBS
For simplification we can say that the surface of the interface of solid (or edge) is not trimmed

## Slide 16: Solid
Background grid
STL triangles defining boundary of Stl
-.- Coupling surface () : Can be created with stl

## Slide 17: Penalty (deformation penalty for coupling)

## Slide 21: Goal:
Quadrature point Geometries (Boundary of Solid)
Quadrature point Geometries (Boundary of Shell)
Coupling Geometries

## Slide 22: Created two examples
Cuboid with faces parallel to cartesian axis Example 02
Cuboid with faces not parallel to cartesian axis
Example 03

## Slide 23: Before implementation
  For both cases the brep_ids of the shell curve in the coupling interface is [6]
Queso model part Dirichlet BCs
Queso model part Neumann BCs (coupling interface)
Cocodrilo: Support, Support Rotational (coupling interface)
Cocodrilo: LoadCondition

## Slide 24: Before implementation
Get Geometry of IgaModelPart which lies on the coupling interface (curve)
Create PointerVector<Geometry<Node>> to store master(solid) and slave(shell) geometries and IntegrationPointsArrayType to store the local coordinates for every integration point of coupling interface of the solid
Loop on Neumann Conditions of Solid (where integration points are):
  Pass Geometry of condition to PointerVector of the master (the geometries are quadrature point geometries)
  Project integration point of the solid to Geometry of IgaModelPart and obtain local coordinates and store it to IntegrationPointsArrayType
Create Quadrature Point Geometries using the Geometry of IgaModelPart
Loop and create Coupled_Quadrature_Point_Geometries
Combine Solid and Shell (this step in not done in the beginning because combination reorders the IDs of the geometries of shells and solids to avoid having the same id. In step 1 we need to take the geometry by knowing the ID of the geometry which lies on the interface)

## Slide 25: Example 02

## Slide 26: Example 02

## Slide 27: Example 02

## Slide 28: Example 03
Queso Neumann BCs
Queso Dirichlet BCs

## Slide 29: Example 03

## Slide 30: Example 03

## Slide 31: Questions:
1. NumberOfShapeFunctionDerivatives : is that the order of the derivaties that we want to store?
2. IntegrationInfo is not used because we have already the integration points
3. On Coupled_Quadrature_Point_Geometries the master(solid) geometry is QuadraturePointGeometry and for the slave(shell) QuadraturePointCurveOnSurfaceGeometry. Shouldn’t the master(solid) geometry be QuadraturePointSurfaceInVolumeGeometry ?
4. For QuESo: Integration points for Dirichlet_BCs are 1 per triangle while for Neumann BCs are for 3 per triangle. Why is that?

## Slide 32: Questions:
Note: For queso integration points for Dirichlet BCs are 1/triangle and for Neumann 3/triangle, no matter the polynomial order of polynomial degree of the shape functions associated with the “finite elements” used in the 3D background grid.
My understanding is that for each triangle we have a discretization with 3 nodes and linear shape function associated to them. They are the boundary representation of the volume and they don’t depend from the polynomial degree of the shape functions of the background grid. There is just a mapping of the nodes and their shape functions of each triangle with the CPs and parametric space of the background grid. The deformations on the b-rep of the solid will be of continuity C1 ?
Similarity with shells?
trimming curve is a curve of degree p=1 (linear shape funciton). We want to apply Dirichlet BCs with penalty on Γ1 . If there is no refinement of the trimming curve the integration points of will be the same. We don’t care about any refinement of the surface
trimming curve Γ1
surface

## Slide 33: Next steps
Create coupling condition including the coupling geometries
Start inserting parameters on the process to be easier (for example choosing the b_rep id from the shell, choosing which models to combine, which model to delete by name)

## Slide 34: Coupling interface area instead of line
See Chapter 2.1 from https://www.sciencedirect.com/science/article/pii/S0045782512003337
Express displacement field of shell body as a function of mid-surface displacement field
v: Displacement field of midsurface

## Slide 35: Integration points for Neumann BCs (QueSo)
Integration rule for triangles:
t is constant
2
1
3

## Slide 36: Quadrature points for triangles
https://mathsfromnothing.au/triangle-quadrature-rules/
In Queso we take 3 integration points. They are more than 1 so we are on the safe side

## Slide 37: Integration points on the boundaries for Solid

## Slide 38: Integration points on the boundaries for Solid
C:\QuESo\queso\containers\triangle_mesh_interface.hpp
For triangular elements Jacobian = const = area of triangle

## Slide 39: Integration points on the boundaries for Solid
C:\QuESo\queso\containers\triangle_mesh_interface.hpp
2
1
3